## Slide 1: Sequential Logic
●
Incorporates memory – holds its Two main types
value.
●
–
Synchronous:
●
Logic (output) changes states in reference to Typically referenced to a clock edge.
a clock
input.
●
–
Asynchronous:
●
Logic changes states
in reference
to any data
input.
Async. Logic
inputs
outputs
Sync.
Logic
clk
inputs
outputs

## Slide 2: Sequential Logic
●
Functional Description:
–
Incorporates memory – holds its value. Involves register assignments within an
always block.
Typically uses non­blocking assignments “<=”.
The sensitivity list indicates whether the logic is sync. or async.
–
–
–
●
Async:
always@(inputs)
outputs <= func(inputs);
Sync:
always@(posedge clock) outputs <= func(inputs);
●

## Slide 3: Sequential Logic
●
Functional Description:
Incorporates memory – holds its value. Involves assignments within an process block.
Uses non-­blocking assignments “<=”.
A VHDL Counter: clk is STD_LOGIC &
cnt is STD_LOGIC_VECTOR.
…
use ieee.std_logic_unsigned.all;
…
process (clk)
begin
if clk='1' and clk'event then
cnt <= cnt + 1;
end if;
end process;

## Slide 4: Synchronous Sequential Logic
●
Inputs
–
Can be synchronous or asynchronous
●
It is important to know the specific functions and requirements of the input data.
From another sync. logic block? Referenced to the same or another clock? Typically sync. logic with same clock.
●
●
●
●
Outputs
–
Exhibit a delay w.r.t the clock.
●
Not all outputs change at the same time. Require timing analysis in implementation.
●

## Slide 5
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity example_01 is
port (
clk: in STD_LOGIC;
switch: in STD_LOGIC_VECTOR(3 downto 0);
led: out STD_LOGIC_VECTOR(3 downto 0)
);
end example_01;
architecture behavioral of example_01 is
begin
process (clk)
begin
if (clk'event and clk='1') then
led(3) <= switch(2);
led(2) <= switch(3) and switch(2);
led(1) <= switch(3) or switch(2);
led(0) <= '0';
end if;
end process;
end behavioral;

## Slide 6
library ieee;
use ieee.std_logic_1164.all;
entity ?? is
port(clk : in std_logic;
s_in : in std_logic;
s_out : out std_logic);
end ??;
architecture behavioral of ?? is
begin
process (clk)
begin
if (clk'event and clk='1') then
s_out <= sin;
end if;
end process;
end behavioral;

## Slide 7
library ieee;
use ieee.std_logic_1164.all;
entity ?? is
port(clk : in std_logic;
s_in : in std_logic_vector(1 downto 0);
s_out : out std_logic_vector(3 downto 0));
end ??;
architecture behavioral of ?? is
begin
process (clk)
begin
if (clk'event and clk='1') then
case s_in is
when "00" => s_out <= "0001";
when "01" => s_out <= "0010";
when "10" => s_out <= "0100";
when "11" => s_out <= "1000";
when others => s_out <= "0000";
end case;
end if;
end process;
end behavioral;

## Slide 8
library ieee;
use ieee.std_logic_1164.all;
entity ?? is
port(clk : in std_logic;
s_in : in std_logic;
s_out : out std_logic);
end ??;
architecture behavioral of ?? is
signal temp : std_logic_vector(7 downto 0);
begin
process (clk)
begin
if (clk'event and clk='1') then
temp <= temp(7 downto 1) & s_in;
end if;
end process;
s_out <= temp(7);
end behavioral;

## Slide 9: Sequential Design Problem
●
Edge Detector (Rising and Falling)
–
Develop a functional description of a edge detector based on the following schematic:
Z-1
in
Which output is the rising/falling edge? Where is the clock?
What are the signals?
How does this translate into code?
Where is the memory (sequential) logic?
How does this translate into code?
Where is the combinational logic?
How does this translate into code?